## Slide 1
Coordinate system Transformation
Elaborated and scripted by Mahdi abdrahmen Madi M1 TPT

## Slide 2
01
A brief introduction to coordinates systems
02
Why is it necessary to transform coordinates from geographic to projected system ?
03
Application
04
Final thoughts
Table of Content

## Slide 3
Our Workflow
Addressing the problem and why is it necessary to transform coordinates ?
Converting those methods to scripts
Understanding the methods behind transforming coordinates
Simplify the scripts used as much as possible

## Slide 4
is usually considered to be 6,371km
The global average value
Is the distance from the center of the earth to a point on or near its surface
definition
A minimum radius of nearly 6,357km denoted b
Polar radius
A maximum radius of nearly 6,378km denoted a
Equatorial radius
The earth Radius

## Slide 5
The Geographic coordinate system (GCS)
is a spherical or ellipsoidal coordinate system for measuring and communicating positions directly on the earth as latitude and longitude It is the simplest, oldest and most widely used of the various of spatial reference systems that are in use and forms the basis for most others. Although latitude and longitude form a coordinate tuple like a cartesian coordinate system, the geographic coordinate system is not cartesian because the measurements are angles and are not on a planar surface

## Slide 6
The Projected coordinate system (PCS)
A projected coordinate system is defined on a flat, two-dimensional surface, has constant lengths, angles, and areas across the two dimensions. A PCS is always based on a GCS that is based on a sphere or spheroid.
In a PCS, locations are identified by x,y coordinates on a grid, with the origin at the center of the grid. Each position has two values that reference it to that central location. One specifies its horizontal position and the other its vertical position. The two values are called the x-coordinate and y-coordinate. Using this notation, the coordinates at the origin are x = 0 and y = 0.

## Slide 7
Addressing the issue :
Why is it necessary to convert coordinates from geographic
to projected ?

## Slide 8
Defines where the data is located on the earth’s surface
Geographic coordinate system (GCS)
Is flat (2D) and records locations in linear units (usually in meters)
Projected coordinate system
Is round (3D) and records locations in angular units (usually in degrees)
Geographic coordinate system
Tells us how to draw the earth on a flat surface
Projected coordinate system (PCS)
To put it simply..

## Slide 9
Convert angular to cartesian coordinates
Convert spherical arc length to great circle distance
Call for the user input depending on the need
Convert cartesian to angular lat/lon coordinates
Convert great circle distance to spherical arc length
About this script

## Slide 10
def latlon_to_xyz (lat,lon) :
Declaring a new function latlon_to_xyz where :
lat = latitude and lon = longitude are its variables
R = 6371
Earth radius in meters
Theta = math.pi/2 – math.radians(lat)
Polar angle
Geographic to
Projected coordinates system
This function allows conversions from angular to cartesian coordinates
Phi = math.radians(lon)
Azimuthal angle

## Slide 11
X = r * math.cos(theta) * math.cos(phi)
the x-axis goes through long,lat (0,0), so longitude 0 meets the equator
Y = r * math.sin(theta) * math.cos(phi)
the y-axis goes through (0,90)
Z = r * math.sin(theta)
and the z-axis goes through the poles.
Geographic to
Projected coordinates system
Return [x,y,z]
Output in meters

## Slide 12
def = xyz_to_latlon (x,y,z) :
Declaring a new function xyz_to_latlon
where : lat and lon are its variables
R = math.sqrt(x**2 + y**2 + z**2)
Radial distance
Theta = math.asin(z/r)
Polar angle
Projected to
Geographic coordinates system
Convert cartesian to angular lat/lon coordinates
Phi = math.atan2(y,x)
Azimuthal angle

## Slide 13
lat = math.degrees(theta)
latitude is the 90deg - zenith angle in range [-90°;90°]
lon = math.degrees(phi)
longitude is the azimuthal angle in range [-180°;180°]
return [lat,lon]
Output of xyz_to_latlon function as latitude,longitude
Projected to
Geographic coordinates system

## Slide 14
def arc_to_deg (arc)
Declaring a new function named arc_to_deg where arc is its variable
return float(arc)/6371/1000 * 180/math.pi
Returns great circle distance in degrees
Convert Spherical arc length[m]
To Great circle distance[deg]

## Slide 15
def deg_to_arc (deg)
Declaring a new function named deg_to_arc where deg is its variable
return float(deg)*6371*1000 * math.pi/180
Returns spherical arc length in meters
Convert Great circle distance[deg] To Spherical arc length[m]

## Slide 16
Measurements
Accurate measurements when using spatial analyst tools such as measuring distances, angles, shapes and directions
Alignment
The coordinates transformations (from GCS to PCS) allows data to be perfectly aligned when going from a 3D model to a 2D flat surface
Location accuracy
And If you won’t be performing queries based on location and distance, GCS can still get the job done
Transferring data
However, when transferring data, it is best advised to convert coordinates back to GCS
Final thoughts
A
M
T
L

## Slide 17
Thank You
see more about this project on GitHub click here